ATI sonic configuration
serial port: 9600 E 7 1
Data quality algorithm (ON)
Shadow correction (ON)
Remove RH from temp calc (ON + RH=0)
U,V,W,Ts @ 10hz output
A sonic anemometer and requisite datalogging setup are included in this shipment:
- ATI sonic anemometer with
  - 50' cable
  - extension boom
  - some U-bolts
- Fiberglass enclosure with
  - datalogger (CR1000)
  - keyboard display + cable
  - battery + regulator/charger
  - AC/DC power supply
- Additional supplies:
  - two CompactFlash memory cards; all-in-one card reader and case
  - power cable for separate 12VDC auto/marine battery
  - cross-over ethernet cable for datalogger communication
  - usb-serial adapter for (last resort) datalogger communication
  - LoggerNet install CD
##### Software setup
The software settings of the sonic anemometer have been pre-set for operation with the datalogger so the sonic is ready to go upon power-up. The settings used are described here in case they are necessary.

The datalogger is ready to use after brief initial setup. It is recommended to complete the initial setup before inserting a memory card.
- Update current date/time
- Review/change constants

To modify program constants, the datalogger must be running. Navigate to the Const Table submenu of the main program menu, select a parameter to modify and press 'Enter' to receive a new value prompt; enter a new value or press 'Cancel'. The datalogger will recompile using the new parameters.

Modifiable constants
	Default	Units	Valid entries
DAYS_OF_DATA_STORAGE	14	days	-1 to autoallocate or a positive integer # of days (within bounds of card space)
STOP_WHEN_FULL	1 (True)	--	0 to ring-fill cards; 1 to stop-fill
AZIMUTH	0	degEofN	0-359; bounds not enforced
DECLINATION	0	degEofN	-90 to 90; bounds not enforced

The azimuth and declination are incorporated into instantaneous wind speed & direction calculations, as well as in generated statistics. Specific values used are recorded in the info data table.
##### Hardware setup
Enclosure
1. If mains 120VAC power is available, plug in the grounded polarized 3-prong outlet leading to the AC adapter mounted below the datalogger. The system will use this power source and float-charge the battery(s).
2. If an auto/marine battery is available, locate the cable with red/black spring clamps. Plug the 2-prong molex connector into the regulator/charger terminals marked BATTERY - External Rechargeable Battery and attach the clamps to (+)/red and (-)/black battery terminals.
3. If the keyboard display is not attached, plug the cable into the CS I/O port of the datalogger.
Sonic anemometer
1. Mount securely
2. Attach cable and route into fiberglass enclosure
3. Connect positive and negative leads of power (red/black) cable to datalogger 12V and G terminals, respectively.
4. Connect serial cable to matching DB9 plug mounted to enclosure
##### System On/Off
The system can be turned off and on as a whole using the small, labeled switch on the battery charger/regulator mounted below the datalogger.
##### Program operation
Upon powering up, the program will automatically begin measuring and recording data. The user can start/stop the recording of data by setting the Recording? menu item of the main menu to either Yes or No. If power is interrupted, the datalogger will resume recording data when power is restored.
Data from the sonic anemometer can be viewed in real-time by selecting the 10Hz data submenu from the main program menu. Instant wind speed & wind direction are displayed along with raw measurements from the sonic.
A fan is mounted in the enclosure which activates at 30ºC by default. This threshold temperature can be changed via the Fan SP, *C menu item on the main program menu.
##### Data Collection
A CompactFlash memory card must be used to store data since the datalogger itself has a small amount of memory. The retrieval of data is two step: exchange memory cards, then convert the binary files on the card into readable text files.
Memory cards can be safely removed after pressing the labeled white button on the memory card module or anytime the datalogger is powered off; they may be inserted at any time. Prematurely ejecting the memory card will cause data in the buffer to be lost and could cause the data frames to become malformed. Should this occur, the conversion program will typically indicate a repair needs to be performed.
The binary data files on the CF cards can be converted using one of several utilities provided by Campbell Scientific. Of the offerings, CardConvert is the most straightforward. It is part of LoggerNet (see install CD) and is also freely available as part of the PC200W software package [http://www.campbellsci.com/pc200w]. Browse its options, which include the ability to split files by time.
##### Alternative Logger Communication
If there is need to communicate with the datalogger directly, it can be done via the serial interface or network interface.
Setting up the serial interface is straightforward for users comfortable with RS-232 communications but since it has low throughput, the network interface is recommended. [PC200W is restricted to serial communications only; LoggerNet is not]
The network interface can be connected directly to a PC using a cross-over ethernet cable (included). Since the datalogger possesses a static IP address, the PC must either also have a static IP address or have an alternate IP configuration established. Setting an alternate configuration permits your computer to function normally on networks which broadcast IP addresses (DHCP) while still allowing it to 'fall back' to datalogger-compatible options when necessary.
On Windows XP PCs, an alternate configuration can be created by navigating My Computer > Control Panel > Network Connections > Right-click [Local Area Connection-of-interest] > Properties > General tab > Internet Protocol (TCP/IP) [IPV4 if specified] > Properties button > Alternate Configuration tab > Use the following IP address: and fill in these fields:
- IP Address: 192.168.174.xxx
  where xxx is different from the logger, but in the range 1-254. Try using 240
- Subnet mask: 255.255.255.0
The exact navigation path will vary on newer versions of Windows but the procedure is similar.
##### Data Tables
Table name	Record interval	Column name	Units	Description
tsdata	100 ms	Ux	m/s	horz wind
		Uy	m/s	horz wind
		Uz	m/s	vert wind
		Ts	C	sonic (virtual) temp
		diag	bitmap	*
stats	30 min	Uz_Avg	m/s	mean vert wind
		Uz_Std	m/s	vert wind std. dev.
		Ts_Avg	Celsius	mean sonic temp
		Ts_Std	Celsius	sonic temp std. dev.
		WD_rslt_Avg	degEofN	mean resultant wind direction
		WD_rslt_Std	deg	resultant wind direction std. dev.
		WS_sclr_Avg	m/s	mean scalar wind speed
		WS_sclr_Std	m/s	scalar wind speed std. dev.
		WS_rslt_Std	m/s	mean resultant wind speed
		baddata_Tot	records	number of flagged sonic data points
		samples_Tot	records	number of data points collected this interval
		inputpwr_Avg	Volts	mean datalogger power source voltage
		panel_temp_Avg	Celsius	mean datalogger panel temperature
info	at every / power-up	sonic_azimuth	degEofN	values used in stats computations
		site_declination	degEofN
		CompileResults	--	post-compile messages from datalogger
		CardStatus	--
		RunSig	--	unique identifiers; detect changes to program
		ProgSig	--

* The diagnostic word is similar to a bitmap but isn't exactly. Data values from the sonic are mapped to consecutive placeholders: Ux, Uy, Uz, Ts = ones, tens, hundreds, thousands columns, respectively. If a data value was -99.99 (transducer error) the corresponding column = 1; if the data value is +99.99 (data quality algorithm rejection) the corresponding column = 2; if the value is NAN, the corresponding column = 3; for no flags, the corresponding column = 0. In the event of a data value being flagged, the value stored to the time-series table will be “NAN” instead of the flagged value.
If any one of the four data values are invalid, the diagnostic word will be non-zero. A naive comparison (diag > 0) will suffice for basic filtering. To identify the reason for flagging, the diagnostic word can be decomposed using the above description.
##### Troubleshooting
Datalogger warns card is not being used: card was not blank and logger is refusing to overwrite data
- safely eject the card and insert a blank one instead OR
- navigate to the System Menu > PCCard > Format card (and lose any data on card)
No data from sonic anemometer
- 12V power present? polarity is correct?
- serial dongle wiring disturbed? (is labeled on dongle cord)
- software settings of sonic anemometer correct? may need to connect w/ PC to check/modify

- Patrick O'Keeffe
pokeeffe@wsu.edu